This Vehicular Charger is used for charging a radio (or battery alone) when inside a vehicle. The charger senses the type of battery inserted and controls the rate of charge accordingly. A battery will be charged at a rapid rate until it is >90% charged and then it will trickle charge until the battery is at >95%. The charger will then switch to a maintenance mode to keep the battery fully charged.

The charger is also equipped with IMPRES™battery communication capability, so can log charging events and data in the IMPRES battery, and also Indicate when the IMPRES battery needs reconditioning / calibration*.

The kit includes the charger, trunnion mounting bracket and wire harness for connection to the vehicle’s electrical system.

The NNTN7616 Tri-Chemistry Vehicular Charger is designed and approved to charge the following batteries for MOTOTRBOseries portable radios:

PMNN4065NiMH 1300mAh IP57 Battery

PMNN4066Li-Ion 1500mAh IMPRES IP57 Battery

PMNN4069Li-Ion 1400mAh IMPRES FM IP57 Battery

PMNN4077Li-Ion 2150mAh IMPRES IP57 Battery

The NNTN7618 Tri-Chemistry Vehicular Charger is designed and approved to charge the following batteries for the Professional seriesportable radios :

HNN4001NiMH 1800mAh IMPRES Battery

HNN4002NiMH 1700mAh IMPRES FM

HNN4003Li-Ion 2350mAh IMPRES IP54 Battery

HNN9008NiMH 1500mAh Battery

HNN9009NiMH 1900 mAh Battery

HNN9010NiMH 1800mAh FM Battery

HNN9011NiCd 1200mAh FM Battery

HNN9012NiCd 1300mAh Battery

HNN9013Li-Ion 1500mAh Battery

NNTN5510Li-Ion 1480mAh ATEX Battery

BatteryVehicular Charger Specification

Voltage11-16 Vdc (13.6V Nominal)Maximum

Charge Rate1250mA +/-15%

Rapid Charge Cycle3 hours typical, depending on battery type, capacity and state of charge

Size94 x 94 x 135 mm

Weight0.9kg (approx)

Operating Temperature+5°C to +45°C

Inline FusesAGC 2 Amp and AGC 0.25 Amp

Part No.	Description

NNTN7616A	MOTOTRBO Vehicular Charger

NNTN7618A	GP Vehicular Charger